Geomorphic Cluster

Channel Condition natural channel no structures, no berms, no downcutting, no lateral cutting past channel alteration, recovered channel recovered banks no or well set back berms providing access to floodplain altered channel < 50% riprap or channelized excess aggradation constricting berms (or) braided channel severely altered channel > 50% rip rap or channelized active downcutting; active widening berms block floodplain access (one or both banks) 10 7 3 1 Hydrologic Alteration over bank flooding = 1½ - 2 years no channel incision no water withdrawals no dams full access to flood plain over bank flooding = 3 - 5 years limited channel incision (or) minor water withdrawal not affecting available biota habitat over bank floods = 6 - 10 years channel deeply incised (or) significant water withdrawal affects biota habitat during low flow no over bank flooding deeply incised structures block access to floodplain (or) severe loss of low flow habitat from water withdrawal (or) flooding yearly or more frequent 10 7 3 1 Deviation from Bankfull Width (WBKFL) none channel at bankfull width +/- < 10% channel 10 - 20% greater than expected bankfull width channel > 20% but < 50% of expected bankfull width channel > 50% greater than expected bankfull width 10 7 3 1 Bank Stability stable Bank Height = Bankfull height > 33% of eroding surface on outer bends protected by roots extending to base flow moderately stable Bank height = Bankfull height < 33% of eroding surface on outer bends protected by roots extending to base flow moderately unstable Bank height > 1½x Bankfull height active erosion on outside bends (overhang, annual tree loss, some slope failure) banks typically high unstable Bank Height ≥ 2x Bankfull height active erosion on straight or inside bends with numerous slope failures, tree loss annually, trees absent 10 7 3 1

Fisheries Cluster

Instream Fish Cover Cover types: LWD, deep pools, overhanging vegetation, boulders/large cobble, deep riffles, undercut banks, thick root mats, dense macrophyte beds, isolated/backwater pools >7 cover types 6 - 7 cover types 4 - 5 cover types 2 - 3 cover types 0 - 1 cover type 10 8 5 3 1 Riparian Zone natural vegetation extends > 2 bankfull widths on each side natural vegetation extends ≈ 1 - 2 bankfull widths on each side natural vegetation extends ≈ ½ bankfull width on each side natural vegetation extends ≈ ⅓ bankfull width on each side (or) filtering function moderately compromised natural vegetation extends < ⅓ bankfull width on each side, (or) lack of regeneration (or) filtering function severely compromised 10 8 5 3 1 Pool Status deep pools common 5 feet or more at base flow present, not abundant depth ≥ 3 feet at base flow present, shallow depth < 3 feet at base flow absent or very shallow 10 7 3 1 Canopy > 75% shaded in reach and upstream 2 - 3 miles well shaded > 50% shaded in reach (or) > 75% in reach but upstream 2 - 3 miles poorly shaded 20 - 50% shaded in reach < 20% shaded in reach 10 7 3 1 Fish Barriers none seasonal withdrawals inhibit movement obstructing vegetative debris within reach structures < 1’ drop within reach structures > 1’ drop within 3 miles structures > 1’ drop within reach 10 8 7 5 3 1

Water Quality Cluster

Water Appearance very clear or tea colored objects visible at 3’ - 6’ no oil sheen no film on submerged objects or rocks occasionally cloudy, clears rapidly objects visible at 1½’ - 3’ may be slightly green no oil sheen mostly cloudy objects visible at ½‘ - 1 ½’ pools may be pea green submerged objects with green film (or) odor of ammonia or rotten eggs very turbid usually objects visible at < ½’ pools bright green obvious pollutants, scum, sheen, foam, floating algal mats (or) strong odor of pollutants 10 7 3 1 Nutrient Enrichment clear along entire reach diverse aquatic plants low quantities of many macrophytes little algal growth fairly clear or slightly greenish moderate algal growth on substrates greenish water lush green macrophytes abundant algal growth especially in warmer months pea green, gray or brown clogging macrophytes severe algal blooms thick algal mats 10 7 3 1 Temperature Range optimal year round for salmonid species present summer or winter temperatures rarely & briefly in stress range no effect on population temperatures frequently reach stress range, thermal kills occur once every 5 - 10 years, periodic impacts on population sustained major thermal stress occurs at least annually, population depressed due to thermal effects 10 7 3 1 Manure Presence * none evidence of livestock access to riparian zone occasional in stream/on banks or waste storage on floodplain extensive on banks or in stream (or) untreated sewage discharge No Score 5 3 1

Invertebrate Cluster

Insect/Invertebrate Habitat Habitat types: fine woody debris, submerged logs, leaf packs, undercut banks, coarse gravel, cobble, boulders ≥ 5 habitat types, at correct stage for colonization 3 - 4 habitat types, some potential habitat 1 - 2 habitat types, substrate covered or scoured at high flows 0 - 1 habitat type 10 7 3 1 Riffle Embeddedness * gravel/cobble < 20% embedded gravel/cobble 20 - 30% embedded gravel/cobble 30 - 40% embedded gravel/cobble > 40% embedded gravel/cobble in riffle completely embedded 10 8 5 3 1 Macroinvertebrates * Group I with good diversity (mayflies, stoneflies, caddis, hellgrammites) Group II dominates (damselflies, dragonflies, sowbugs, blackflies, crayfish) Group III dominates (midges, craneflies, horseflies, leeches, worms) very reduced number of species or near absence of all macroinvertebrates 15 6 2 -3

| * score only if applicable |  | Channel Forms | Entrenchment | W/D | Sinuosity | Slope |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Aa+ | Very steep, deeply entrenched, torrent streams | < 1.4 | < 12 | 1.0 – 1.1 | > .10 |
| Dominant Substrate Material |  | A | Steep, entrenched, cascading, step/pool streams | < 1.4 | < 12 | 1.0 – 1.2 | .04 - .10 |
|  |  | B | Moderately entrenched, moderate gradient, riffle dominated channel with infrequently spaced pools | 1.4 – 2.2 | > 12 | > 1.2 | .02 - .039 |
| 1 = 2 = 3 = 4 = 5 = 6 = | bedrock boulders cobble gravel sand silt/clay |  | C | Low gradient, meandering, point-bar, riffle/pool, alluvial channels with broad well defined floodplains | > 2.2 | > 12 | > 1.4 | < .02 |
|  |  |  | D | Braided channel with longitudinal & transverse bars | n/a | > 40 | n/a | < .04 |
|  |  |  | DA | Anastamosing narrow & deep with extensive, well vegetated floodplains & associated wetlands | > 2.2 | Highly variable | < .005 |
|  |  |  | E | Low gradient, meandering riffle/pool stream with low width/depth ration & little deposition | > 2.2 | < 12 | > 1.5 | < .02 |
|  |  |  | F | Entrenched, meandering riffle/pool channel on low gradients with high width/depth ratio | < 1.4 | > 12 | > 1.4 | < .02 |
|  |  |  | G | Entrenched “gully” step/pool and low width/depth ratio on moderate gradients | < 1.4 | < 12 | > 1.2 | .02 - .039 |

| Date: | / / |  | Survey Party: |  |
| --- | --- | --- | --- | --- |
| Chapter: |  |  | # |  |  | DEC Region: |  |
| County: |  |  | Township: |  |
| Watershed Code: |  |  | Watershed Index # (HUC): |  |  | Stream: |  |
| Reach: |  |
| Coord’s: |  | N |  |  | W |  | Drainage Area: |  | sq. mi. |
| Reach Length: |  | Ft. |  | Active Floodplain Width: |  | Ft. |  | Bankfull Width: |  | Ft. |
| Dominant Substrate: |  | (1 – 6) |  | Channel Form: |  | (Aa+ - G) |  | Valley Type: |  | (I – IX) |
| Land Use in Drainage Area (%): | Row crop |  | Hayland |  | Grazing |  | Forest |  |
|  | Confined animal feeding |  | Conservation reserve |  |
|  | Industrial/Commercial |  | Residential |  | Other |  |

| See protocol & field book summary sheet for specific criteria. | Rankings (weighted 15 to -3 scale) |
| --- | --- |
| Item |  | Score |  | Optimal Severely impacted |
| Geomorphic cluster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Channel Condition |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Hydrologic Alteration |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Deviation from Wbkfl |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Bank Stability |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Fisheries cluster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Instream Fish Cover |  |  |  | 10 |  | 8 |  |  | 5 |  | 3 |  | 1 |  |
| Riparian Zone |  |  |  | 10 |  | 8 |  |  | 5 |  | 3 |  | 1 |  |
| Pool Status |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Canopy |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Fish Barriers |  |  |  | 10 |  | 8 | 7 |  | 5 |  | 3 |  | 1 |  |
| Water quality cluster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Water Appearance |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Nutrient Enrichment |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Temperature Range |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Manure Presence * |  |  |  |  |  |  |  |  | 5 |  | 3 |  | 1 |  |
| Invertebrate cluster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Insect/Invertebrate Habitat |  |  |  | 10 |  |  | 7 |  |  |  | 3 |  | 1 |  |
| Riffle Embeddedness * |  |  |  | 10 |  | 8 |  |  | 5 |  | 3 |  | 1 |  |
| Macroinvertebrates * |  |  | 15 |  |  |  |  | 6 |  |  |  | 2 |  | -3 |
| * NOTE: These items are optional on the Stream Visual Assessment Protocol |  |

| Average score for reach: |  |  | Status: | Poor | Fair | Good | Excellent |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | < 6.0 | 6.1 – 7.4 | 7.5 – 8.9 | > 9.0 |
| (Total divided by number of elements scored) |  |  |  |  |  |  |
| Reference reach candidate: | Yes |  | No |  | Possible |  |  |

| Additional studies needed: |  |
| --- | --- |

| Summary of observed problems: |  |
| --- | --- |

| Suspected causes: |  |
| --- | --- |

| Options/Recommendations: |  |
| --- | --- |

| Field Sketch: |  |
| --- | --- |
|  | Banks identified facing downstream. |